## Slide 1: RVI - Dynamic Agents
Agent

## Slide 2
Purpose
Deploy remote probes
to monitor vehicles
and report results

## Slide 3
Overview
Agent Server
TCU
ECU 2
Agent Server [Cloud] Distributes dynamic agents over the air, using RVI, to vehicle TCUs
TCU [Head Unit] Executes dynamic agents in background to monitor ECU data streams
Big Data [Cloud] Receives and analyses reports transmitted from dynamic agents through RVI
ECU 1
Big Data
RVI

## Slide 4
Anomaly monitor agent reads data from vehicle buses
Any anomalous data detected by the agent is reported to the big data server
Big data server profiles all incoming data to generate failure trends and analysis
Use case: Health Monitor
Anomaly Monitor
Vehicle
Big Data Server
Anomaly tracker
TCU
ECU
RPM=650
SPD=140
SPD=140 | RPM=650
!
VIN: SAJ…, Speed-RPM mismatch, RPM: 6.. VIN: SAL…, Excessive CAN resend, Frame: ..
…

## Slide 5
Feature monitor records all in-cabin feature usage
Periodic reports are sent by the feature monitor to the big data server
Feature tracker compiles report of fleet-wide feature usage
Use case: Feature usage
Feature monitor
Vehicle
Big Data Server
Feature tracker
IVI
AM Radio Selected
AM Radio: 235
CD player: 5574
Hill descent: 311
Rear defrost: 9115

## Slide 6
Bluetooth issue agent monitors pairings, streaming, and other possible failure points in the IVI BT stack
Any BT error is logged with circumstances and equipment ID
Error reports are transmitted to backend server for further analysis and bug fixes
Use case: BT issue tracker
Vehicle
BT Stack
BT Agent
!
!
Big Data Server
BT Issue tracker
VIN: SAJ…, Nexus 5, Paring failed. Error: 47 VIN: SAL…, iPhone 6, Stream packet loss. Er..
…