## Slide 1: RVI Dynamic Agents
Anson Fan
Magnus Feuer
Jaguar Land Rover Open Software Technology Center

## Slide 2
Purpose
To create a dynamic agent that runs in the background completely separate from all other processes given a specific task until the expiration date of the agent.
Case by Case Agents
Any RVI Enabled Vehicle
Unified Data Logging
1

## Slide 3
Overview
Case by Case Code
Data Collectors
Script loader and vehicle targeting Web launcher to specify what code to send along with how long and who to send to
Data collectors on the fleet[Raspberry Pi] Receives code and runs independently of all other services and reports if needed
Receive and process data[Big Data Logging] Will either process data in vehicle or send to backend server for data aggregation
Target Vehicle Fleet
Data Aggregation

## Slide 4
Launch agent to send geofence agent with specific perimiter
RVI backend server pushes code to remote client
Agent runs in background and continuously monitors GPS position
If out of bounds detected, start GPS data logging to backend and notify
Case 1 : Geofencing
Launch agent to detect specific reported problem. ex: TPS + ABS both active
RVI backend server pushes code to car models in question
Agent runs in background and monitors TPS + ABS signals
If both signals are triggered at the same time, start complete data logging
Case 2 : Fleet Issues

## Slide 5
Code is uploaded to database to be distributed to target cars and time limit to run code is set.
Server calls an RVI service from all the available connected devices that have been selected.
Agent is transferred to client through service calls.
Agent stays and runs on client until expiration date, reporting back to backend database server if needed.
Backend Loader/Server
Website
Agent Upload
Car Fleet
RVI Agent Handler
RVI Logger
Backend Database

## Slide 6
Virtual Environment
RVI
Register service for dynamic agents onto local RVI .
RVI backend sends signal to download new agent through set up service call.
Download agent and store code in separate temporary local directory.
Code runs until expiration date and interfaces with car as needed.
Send data to backend server if needed and send shutdown signal to server.
Vehicle
Agent Handler
Independent Temporary Storage
Raspberry Pi / Connected Device
Agent Package
Independent Process Run Time

## Slide 7: Thank You
Anson Fan
afan1@jaguarlandrover.com
Magnus Feueur
mfeuer@jaguarlandrover.com